| DATE: | 8 June 2013 | Tow Vehicle (TV): | 2008 GMC Sierra 2500HD CrewCab 2x4 SRW Standard Bed – 153 “ Wheel Base |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Duramax 6.6L V-8 Diesel with Allison Transmission – 3.73 Positive Traction Rear |  |  |
|  | 5th Wheel Travel Trailer: | 2010 Flagstaff 8526RLWS |  |  |  |  |  |  |
|  |  | Weight (lbs) |  |  |  |  |  |  |  |  |  |
| TOW VEHICLE AND CAMPER SPECIFICATIONS | TV Gross Vehicle Weight Rating (GVWR) | 9,200 - Limit |  | Per Door Pillar - maximum the TV can weigh with all options, occupants, cargo, and fuel |
|  | Max Trailer Weight | 15,200 |  | Per Owner’s Manual - maximum a fully loaded 5th Wheel can weigh |
|  | Gross Combined Weight Rating (GCWR) | 24,500 |  | Per Owner’s Manual - maximum combined weight of TV, TT, occupants, cargo, and fuel |
|  | Front Axle Weight Rating Torsion Bar | 4,800 |  | Per Owner’s Manual - maximum the TV front axle can support |
|  | Front Spring Rating | 4,500 - Limit |  | Per Owner’s Manual and Door Pillar |
|  | 2 stage Rear Axle Weight Rating | 6,900 |  | Per Owner’s Manual - maximum the TV rear axle can support |
|  | Semi-Elliptical Spring Rating | 6,084 - Limit |  | Per Owner’s Manual and Door Pillar |
|  | Unladen Weight | 6,419 |  | 150 pound driver and 26 gallons diesel |
|  | 5th Wheel Hitch Rating | 16,000 |  | Pullrite SuperGlide 3300 Manual |
|  | Maximum Rated Pin Weight | 4,000 |  | Pullrite SuperGlide 3300 Manual |
|  | Dry Weight/PIN/AXLE | 7,931/1,169/6762 |  | Per manufacturer – Brochure |
|  | CAMPER UVW | 7,219 |  | Yellow Sticker – AS BUILT |
|  | Camper Axle Rating | 4,000 x 2 - Limit |  | TAG on Lippert Axles |
|  | GVWR – Trailer – Loaded (gross vehicle weight rating) | 9,169 - Limit |  | YELLOW STICKER – UVW PLUS PAYLOAD |
| ACTUAL MEASUREMENTS | TV ALONE – FRONT AXLE | 4,380 |  | Truck loaded for camping – full fuel, family, and gear |
|  | TV ALONE – REAR AXLE | 3,700 |  | Truck loaded for camping – full fuel, family, and gear |
|  | TV ALONE – WEIGHT | 8,080 |  | Truck loaded for camping – full fuel, family, and gear |
|  | TV & CAMPER – FRONT AXLE | 4,380 |  | 4,500 – 4,380 = 120 | remaining capacity calculated by (FGAWR) - (FGAW) |
|  | TV & CAMPER – REAR AXLE | 5,380 |  | 6,084 – 5,380 = 704 | remaining capacity calculated by (RGAWR) - (RGAW) |
|  | TOW VEHICLE WEIGHT | 9,760 |  | 4,380 + 5,380 = 9760 | 9560 – 9200 = 560 pounds Overload |
|  | CAMPER AXLES | 8,020 |  | 8,000 – 8020 = -20 pounds overload |
|  | ACTUAL PIN LOAD | 1,680 |  | 9,760 – 8,080 = 1680 pounds |
|  | CAMPER WEIGHT | 9,760 |  | Pin Load + Axle Load (8,080 + 1,680 = 9,760) 9,760 – 9,169 = 591 pounds OVERLOAD |
|  | COMBINED WEIGHT | 17,580 |  | 24,500 – 17,580 = 6,920 Remaining capacity |
|  | PIN WEIGHT - Actual % (% of Camper on TV PIN) | (1680/9,760) = 0.172 * 100 = 17.2% |  | calculated by (PIN Weight) / (GVW-Trailer-Loaded) x 100 Target range is 15-25% |  |