AUXILIARY OPERATION

The Lippert Hydro-Sync Slideout System can be run with auxiliary power devices

like electric drills, ratchet wrenches or cordless screwdrivers. In the event of

electrical or system failure, this manual method of extending and retracting the

slideout room can be used. A standard handheld drill is all that is required. A

standard 38" room will take approximately 45 seconds to retract. See the

instructions below.

1. Remove protective label. (See Fig. 2).

2. Using a standard hex bit, insert into auxiliary drive device, i.e. cordless drill or

screwdriver or ratchet wrench.

3. Insert hex bit into coupler found under protective label. (See Fig. 3)

4. Run drill forward or clockwise to extend slideout room and in reverse or

counterclockwise to retract slideout room.